## Slide 1
Laser Based Flue Gas Detection
Serial Monitor
Experimental Calculation method
deltaT
ΔP
ΔE
δE
nbCO
nbCOlim
[CO]lim
P | T
t
λ
V
glass
air
CO
Indoor result
Results: Power plant
Problems:
High ambient temperature
Difficulty to compare: with and without gas
Challenge to fix the Laser
Temperature (°C)
>
Time (s)
CO
air
Arduino
Detector
Laser diode
+ collimator
LD controller
temperature controller
Indoor experimental setup
Experiment at the power plant
Serial Plotter
Beer’s law
Concentration <-> absorption
1550nm
0.79990 eV
<=>
CO absorbs Laser Energy
Theory
Time (ms)
>
Temperature (°C)
>
Mariam Mourad@INT/AECENAR 2020
Temperature controller
Laser diode controller
Laser diode
collimator
IR camera: detector
Laser
LD mount
Arduino
Laptop
2 cases: with or without gas
The detector measures the temperatures in fuction of time.
The Arduino Program calculates the variation of temperature deltaT. If the variation is bigger than the usual variation of the Laser itself, the number of the detected gas molecules is calculated nbCO. From the caracteristic table of this system, the corresponding power variation ΔP can be deduced. Knowing the time t wich is the refreshtime of the program, the absorbed energy ΔE is calculated. The wavelength of the laser give us the absorbed Energy by one molecule δE. The quotient of ΔE and δE gives us the nbCO.
The detected volume is separately calculated. It is the product of the width of the chimney and the surface of one pixel (pixel_x*pixel_y).
Because in our special case just one pixel of the 64 is influenced by the radiation.
The volume let us deduce the limit number of molecules which is allowed to measure,
from the limit concentration nbCOlim given by the WHO.
Finally the program compares the measured nbCO with the limit nbCO, and tells us if the gas concentration is environmentally friendly or not.
The gas absorbs the laser energy according to Beer’s law.
That means, the absorption is proportional to the concentration. In this case, the carbon monoxide is studied.
The wavelength of the Laser is 1550nm
which corresponds to an energy of 0.79990eV. This wavelength is usually used to detect the CO. According to the diagram this energy fits between the A2π energy levels.
Schematic
The laser diode controller gives the necessary intensity
and power to the laser diode. The temperature controller fixes the wavelength by fixing the temperature. The collimator lets the radiation be parallel. The laser is produced. It is an infrared one. So an IR detector like the Melexis temperature camera can detect its power. The Arduino reads, converts and processes this information, and gives it to the Laptop.
The serial monitor on the right is like one picture.
Instead a colored pixel a temperature in °C is displayed. The pixels which detect the laser have a higher temperature than the others.
To see if this system really detects CO and
to develop the system, CO is produced by the
dehydration of formic acid with sulfuric acid.
The CO is produced in this hermitically closed
container. And to not forget the influence of this green glass, the 3 cases are compared: nothing in the lasers path (air), an empty container (glass) and the container with CO.
Like you see in the photo left, the result is the serial plotter right.
Arduino do not save the data. This problem was solved by python.
All this was actually done to prove that the power plant at the right is environmentally friendly. This power plant converts waste to electrical energy by heat treatment. The flue gas goes throw several filters. After the last filter the measurements are taken. At the right you see the results of the first real experiment at the power plant.
This experiment was done to see which problems we have at the outdoor experiment to solve them.
During the measurement the gas was environmentally friendly concerning the CO.
But we have to repeat this measurement to ensure
The results and with better conditions.
>